## Slide 1
01/60
CSE 4th Year · WSN
Week 2 — Radio & Physical Layer
Path loss · shadowing · fading · RSSI/LQI/PRR · IEEE 802.15.4 PHY
Lab environment: Instant Contiki 3.0 · old Cooja · VMware

## Slide 2
Week 2 — Radio & Physical Layer
02/60
Week 2 in the course flow
From hardware anatomy to the physics that makes WSN links unstable.
W1
Introduction & hardware
W2
Radio & PHY
W3
Energy
W4
MAC I
W5
MAC II
W6
6LoWPAN
W7
RPL
Today’s anchor
A wireless link is not a cable. It is a probability distribution with packets attached.
Why it matters
Routing, MAC scheduling and energy models become wrong if the PHY assumptions are too clean.
Lab proof
Students will collect RSSI, LQI and PRR inside old Cooja and see model dependence.

## Slide 3
Week 2 — Radio & Physical Layer
03/60
2 × 45 min teaching plan
Keep formulas short; spend time on interpretation and experiment design.
Part A — 45 min
Radio units and propagation
• dB and dBm
• link budget
• receiver sensitivity
• SNR and noise floor
• path loss model
• shadowing and fading
Part B — 45 min
Measurements and 802.15.4
• RSSI, LQI, PRR
• transitional region
• link asymmetry
• IEEE 802.15.4 PHY
• Cooja radio media
• lab walkthrough
Mini-break: ask “what does RSSI NOT tell us?”
Suggested pace: 30 slides per 45 minutes
Skip detailed derivations if students are tired
Use lab slides as the bridge to Week 3 energy

## Slide 4
Week 2 — Radio & Physical Layer
04/60
Learning outcomes
By the end of Week 2, students should be able to reason about links, not just draw circles.
LO1
Compute and interpret dBm, dB and simple link budgets
LO2
Explain path loss, shadowing, multipath and fading qualitatively
LO3
Distinguish RSSI, LQI and PRR without mixing them
LO4
Explain transitional regions and directional link asymmetry
LO5
Recognize core IEEE 802.15.4 PHY facts used by WSN platforms
LO6
Run a Cooja experiment and avoid overclaiming from the radio model

## Slide 5
SECTION
Part A: Radio power and propagation
The physics behind unstable links.
Week 2 section break
05/60

## Slide 6
Part A — radio power
06/60
Why radio is not “just networking”
In WSNs, the communication medium is the environment.
Packets travel as electromagnetic waves, not as abstract arrows
Walls, people, furniture, metal and interference change the channel
Two close nodes may have a poor link; two farther nodes may sometimes work
A link is better modeled as a probability of successful packet delivery
Core idea: link quality = time-varying evidence, not a binary edge

## Slide 7
Part A — radio power
07/60
Transmit power and received power
The transmitter radiates energy; the receiver captures only a tiny fraction.
Tx
Rx
Transmitted power spreads outward; received power is much smaller.
P_dBm = 10 log10(P_mW / 1 mW)
Power is often expressed in dBm
0 dBm = 1 mW
Negative dBm is normal: it means less than 1 mW
−80 dBm is stronger than −90 dBm

## Slide 8
Part A — radio power
08/60
dBm reference table
Students must be comfortable reading negative received-power values.
Power | dBm
100 mW | 20 dBm
10 mW | 10 dBm
1 mW | 0 dBm
0.1 mW | −10 dBm
0.001 mW | −30 dBm
10⁻⁹ mW | −90 dBm
−80 dBm > −90 dBm
Do not drop the minus sign
“Larger” means less negative in dBm
dBm is absolute power relative to 1 mW

## Slide 9
Part A — radio power
09/60
dB versus dBm
Same letters, different meaning — classic exam trap.
dBm
Absolute power level relative to 1 mW.
Example: received signal = −85 dBm
dB
Ratio, gain or loss.
Example: path loss = 70 dB; antenna gain = 2 dB
+3 dB ≈ ×2 power +10 dB = ×10 power −10 dB = ÷10 power

## Slide 10
Part A — radio power
10/60
Link budget
A first-order accounting of gains and losses.
P_r = P_t + G_t + G_r − PL − L_s
P_r: received power in dBm
P_t: transmit power in dBm
G_t, G_r: antenna gains in dB
PL: propagation path loss in dB
L_s: additional system losses in dB
Worked intuition
If P_t = 0 dBm, antennas are 0 dB, path loss is 75 dB and system losses are 2 dB:
P_r = −77 dBm
Now ask: is that above sensitivity, and what is the noise floor?

## Slide 11
Part A — radio power
11/60
Receiver sensitivity is not a cliff
A receiver can decode weak signals only under specified conditions.
Packet delivery (%)
Signal gets weaker → delivery probability falls gradually
Correct interpretation
Sensitivity is the minimum signal level for a given performance target. It is not a magic border where links become perfect above it and impossible below it.

## Slide 12
Part A — radio power
12/60
Noise floor and SNR
RSSI alone is incomplete because receivers also hear noise and interference.
SNR_dB = P_signal,dBm − P_noise,dBm
Case 1
Signal: −80 dBm
Noise: −100 dBm
SNR = 20 dB
Likely better
Case 2
Signal: −80 dBm
Noise: −82 dBm
SNR = 2 dB
Likely poor
A
B
Same RSSI can behave differently.

## Slide 13
Part A — propagation
13/60
Three propagation effects to separate
Students often blend these; keep them distinct.
Path loss
Average signal reduction as distance increases.
Shadowing
Slow variation caused by obstacles and environment structure.
Fading
Shorter-term variation caused by multipath combination.
Received power = average distance trend + obstacle variation + multipath variation

## Slide 14
Part A — propagation
14/60
Path loss
Signal power decreases as energy spreads and interacts with the environment.
Geometric spreading
Absorption
Reflection
Diffraction
Scattering
Penetration through materials
Antenna and polarization effects
Tx
Rx
Longer distance usually means larger average path loss.
PL_dB = P_t,dBm − P_r,dBm

## Slide 15
Part A — propagation
15/60
Free-space model
Useful reference, but too clean for indoor WSNs.
PL_FS(d) = 20 log10(4πd / λ)
λ = c / f
At 2.4 GHz
λ ≈ 0.125 m
At 1 m: PL ≈ 40 dB
At 10 m: PL ≈ 60 dB
×10 distance → +20 dB loss in free space
Path loss grows logarithmically

## Slide 16
Part A — propagation
16/60
Log-distance path loss
Real rooms often attenuate faster than free space.
PL(d) = PL(d₀) + 10n log10(d/d₀)
n = path-loss exponent
n = 2 in ideal free space
n is larger indoors or around obstacles
Estimate n by measurement when possible
Example
PL(1 m) = 40 dB
n = 3
At 10 m:
PL = 40 + 30 log10(10)
PL = 70 dB
So the same distance can cost 10 dB more than free space.

## Slide 17
Part A — propagation
17/60
Shadowing
Distance trend is average behavior; obstacles create deviations.
Concrete wall
Metal cabinet
Human body
Dense vegetation
Industrial machinery
Vehicle or moving object
PL(d) = average path loss + Xσ
Shadowing is large-scale variation around the average path-loss trend.

## Slide 18
Part A — propagation
18/60
Log-normal shadowing model
A simple way to represent “same distance, different received power.”
PL(d) = PL(d₀) + 10n log10(d/d₀) + Xσ
RSSI samples at similar distance
Interpretation
The deterministic term gives the average. The random term represents deviations caused by environment structure. Larger σ means stronger variability.

## Slide 19
Part A — propagation
19/60
Multipath propagation
A signal can arrive through several delayed paths.
Tx
Rx
Direct path + reflected paths combine at receiver.
Mechanisms
Reflection, diffraction and scattering cause multiple copies with different amplitude, phase, delay and direction.

## Slide 20
Part A — propagation
20/60
Constructive and destructive interference
Multipath components may reinforce or cancel each other.
Constructive
Components arrive with similar phase → amplitude increases → stronger received signal.
Destructive
Components arrive with opposing phase → partial cancellation → weaker received signal.
At 2.4 GHz, λ ≈ 12.5 cm — moving a mote a few cm can matter

## Slide 21
Part A — propagation
21/60
Fading
Received signal variation caused by channel changes.
RSSI over time
Slow fading
Channel changes slowly relative to packet transmission.
Fast fading
Channel changes significantly over a short time.
Static nodes still fade
People, doors, vehicles, machinery and reflecting objects move.

## Slide 22
Part A — propagation
22/60
Flat versus frequency-selective fading
For Week 2, keep the intuition; deeper math belongs to wireless comms.
Flat fading
All frequency components are affected approximately equally. Signal amplitude changes, shape mostly preserved.
Frequency-selective fading
Different frequency components experience different attenuation and phase shift. Waveform distortion can occur.
Whether fading is flat depends on bandwidth and multipath delay spread

## Slide 23
Part A — propagation
23/60
Combined received-power model
A compact mental model for simulation and measurement.
P_r(d,t) = P_r(d₀) − 10n log10(d/d₀) − Xσ + F(t)
Distance trend
Average loss increases with d
Shadowing
Obstacle-dependent deviation
Fading
Short-term multipath variation
Conclusion: received power is not a deterministic function of distance

## Slide 24
Part A — propagation
24/60
Distance is not a reliable link-quality metric
Two equal-length links can behave differently.
Tx
Rx
Link A: same distance, clear path
Tx
Rx
Link B: same distance, wall + metal + body
Wall material
Antenna orientation
Node height
Metal objects
Human movement
Interference
Multipath propagation
Use measurement, not geometry alone

## Slide 25
SECTION
Part B: Link-quality metrics
RSSI, LQI and PRR are related, not interchangeable.
Week 2 section break
25/60

## Slide 26
Part B — metrics
26/60
Metric stack
Each metric answers a different question.
RSSI
How strong was the received signal power?
LQI
How good was the successfully received frame?
PRR
How often did packets actually arrive?
Hardware evidence + empirical delivery evidence = better link reasoning

## Slide 27
Part B — metrics
27/60
RSSI: Received Signal Strength Indicator
RSSI is received power evidence, not delivery probability.
RSSI ≈ received power during packet reception
Usually reported in dBm or a platform-specific integer scale
Available from many radio chips
Can support localization, topology control and link selection
Collected only when something is received
RSSI tends downward but not smoothly

## Slide 28
Part B — metrics
28/60
Interpreting RSSI
Approximate labels help, but thresholds are platform dependent.
RSSI | Interpretation
−50 dBm | Very strong
−70 dBm | Moderate
−85 dBm | Weak
−95 dBm | Very weak
Receiver sensitivity
Noise floor
Interference
Radio implementation
Packet length
Hardware calibration
Do not copy an RSSI threshold blindly between platforms

## Slide 29
Part B — metrics
29/60
RSSI limitations
Strong RSSI helps, but it does not guarantee delivery.
RSSI can mislead
• includes interference/noise
• varies over time
• differs across hardware
• does not fully represent decoding quality
Two classic cases
• strong RSSI + collision → bad PRR
• moderate RSSI + low noise → good PRR
RSSI is one piece of evidence.
Use with
Noise floor, LQI, PRR, retransmissions and application delivery behavior.

## Slide 30
Part B — metrics
30/60
LQI: Link Quality Indicator
LQI is receiver-specific quality evidence for a received frame.
LQI = implementation-dependent frame-quality indication
May use correlation, SNR, signal strength, estimated chip errors or combinations
Associated with a successfully detected packet
Not a universal unit like metres, watts or dBm
Do not compare LQI from different radio families blindly
Old Cooja relevance
Sky/TelosB-style simulations often model CC2420-class behavior. Treat LQI as a platform-specific clue.

## Slide 31
Part B — metrics
31/60
CC2420 example
Useful because old WSN literature and Cooja examples often assume CC2420-style radios.
CC2420 reports
• RSSI value
• 7-bit average correlation value
• CRC validity indication
Why it matters
Correlation is related to chip errors, not simply another power measurement.
Teaching phrase
RSSI concerns power.
LQI concerns decoding quality evidence.

## Slide 32
Part B — metrics
32/60
LQI limitations
High LQI on one packet does not prove a stable link.
Hardware-specific meaning
Usually available only for received packets
Cannot describe packets never detected
May saturate on strong links
Single-packet value may not represent long-term reliability
Operating system may transform raw radio values
High LQI for received packets + many missing packets = still a bad link
A
B
Measure the missing packets too.

## Slide 33
Part B — metrics
33/60
PRR: Packet Reception Ratio
PRR directly measures successful delivery over an observation window.
PRR = N_received / N_transmitted
Example
92 received out of 100 transmitted:
PRR = 0.92 = 92%
Empirical metric, not instantaneous hardware value
Depends on observation window
Requires sequence numbers or known transmission count
Most directly reflects application delivery

## Slide 34
Part B — metrics
34/60
Sequence numbers for PRR
Missing sequence numbers reveal lost packets.
received: 1, 2, 3, 5, 6, 9, 10
Missing packets
4, 7 and 8 are absent.
Expected 10, received 7.
PRR = 7/10 = 0.70
Lab rule
Every sender packet must carry a sequence number. Otherwise students cannot distinguish loss from silence.

## Slide 35
Part B — metrics
35/60
PRR window size matters
A short window reacts fast; a long window is stable but slow.
PRR over 10-packet windows
PRR over 100-packet windows
Window choice is part of the measurement design

## Slide 36
Part B — metrics
36/60
Comparing RSSI, LQI and PRR
The three metrics should not be treated as interchangeable.
Metric | Represents | Main limitation
RSSI | received power | not delivery
LQI | quality of received frame | hardware-specific
PRR | successful delivery fraction | needs many packets
Strong RSSI but low PRR: collision or interference
High LQI but low PRR: missing packets are invisible to LQI
Similar RSSI both ways but asymmetric PRR: ACK direction matters

## Slide 37
SECTION
Part C: Transitional links and asymmetry
Where radio stops behaving politely.
Week 2 section break
37/60

## Slide 38
Part C — transitional links
38/60
Three informal link regions
Real links degrade through a transitional zone, not a perfect disk boundary.
PRR vs. distance/intensity
Connected
High PRR, stable connectivity, few retransmissions.
Transitional
Intermediate or highly variable PRR, bursts, asymmetry.
Disconnected
PRR near zero, few decoded packets, unstable discovery.

## Slide 39
Part C — transitional links
39/60
Why the transitional region matters
Marginal links can be more expensive than clearly bad links.
Node appears as neighbor, then disappears
Broadcast may work, ACKs may fail
One channel works, another does not
Routing repeatedly selects and removes the neighbor
Repeated retransmissions waste energy
Shortest geographic link ≠ lowest energy link
A
B
“Almost works” is often expensive.

## Slide 40
Part C — transitional links
40/60
Hysteresis
Avoid rapid topology switching caused by noisy measurements.
Add neighbor if PRR > 0.8; keep until PRR < 0.5
PRR fluctuates around thresholds
Why it helps
One threshold causes rapid add/remove decisions. Two thresholds create a stability band.

## Slide 41
Part C — asymmetry
41/60
Link asymmetry
A → B quality may not equal B → A quality.
A
B
A → B PRR = 0.95
B → A PRR = 0.40
Different transmit power
Receiver sensitivity variation
Antenna orientation
Different local noise floor
Interference near one receiver
Temporary fading

## Slide 42
Part C — asymmetry
42/60
Asymmetry and acknowledgements
A strong data direction is not enough if ACKs cannot return.
P_success = PRR_forward × PRR_reverse
Example
Forward PRR = 0.90
Reverse ACK PRR = 0.50
Exchange success = 0.45
Routing implication
A node may hear advertisements from a parent, select it, then fail to deliver packets in the reverse direction needed by the protocol.

## Slide 43
SECTION
Part D: IEEE 802.15.4 PHY
The low-rate radio foundation used by classic WSN platforms.
Week 2 section break
43/60

## Slide 44
Part D — IEEE 802.15.4
44/60
IEEE 802.15.4 purpose
The PHY/MAC basis for many low-power WSN systems.
Defines
• Physical layer
• MAC sublayer
• Low-rate wireless operation
• Mechanisms for energy-constrained devices
Not the same as Zigbee
Zigbee adds network, application support and profiles above IEEE 802.15.4. Other stacks can also use 802.15.4.
IEEE 802.15.4 ≠ Zigbee

## Slide 45
Part D — IEEE 802.15.4
45/60
Classic 2.4 GHz PHY
The course focus: globally common O-QPSK 2.4 GHz PHY used by many WSN platforms.
Channel | Center frequency
11 | 2405 MHz
12 | 2410 MHz
15 | 2425 MHz
20 | 2450 MHz
25 | 2475 MHz
26 | 2480 MHz
Key numbers
16 channels: 11–26
Channel spacing: 5 MHz
Raw PHY rate: 250 kb/s
Spreading: 2 Mchip/s

## Slide 46
Part D — IEEE 802.15.4
46/60
Data rate versus application throughput
250 kb/s is PHY raw rate, not what your application gets.
PHY headers
MAC headers
Addresses
Sequence numbers
Frame Check Sequence
Security fields
Acknowledgements
Backoff and retransmissions
Application throughput < raw PHY data rate
Usable throughput drops with overhead/load

## Slide 47
Part D — IEEE 802.15.4
47/60
Symbols, chips and DSSS
The 2.4 GHz PHY spreads each 4-bit symbol into a 32-chip sequence.
4 bits → 1 symbol → 32 chips
Rates
250,000 bit/s ÷ 4 = 62,500 symbols/s
62,500 × 32 = 2,000,000 chips/s
DSSS intuition
Direct-Sequence Spread Spectrum spreads information across a wider chip sequence. It can help synchronization and narrowband interference resistance, but it does not make links immune.

## Slide 48
Part D — IEEE 802.15.4
48/60
O-QPSK intuition
Students do not need full modulation math, but they should know the processing chain.
Bits → Symbols → Chip sequences → O-QPSK waveform
O-QPSK
Offset Quadrature Phase-Shift Keying offsets component transitions to limit abrupt phase changes.
Receiver view
The receiver reverses the chain: waveform → chips → symbols → bits, if the signal can be synchronized and decoded.

## Slide 49
Part D — IEEE 802.15.4
49/60
PHY frame: PPDU
The PHY frame wraps the MAC frame.
Field | Size | Purpose
Preamble | 4 bytes | synchronization
SFD | 1 byte | frame boundary
PHR | 1 byte | payload length
PSDU | 0–127 bytes | MAC frame
Maximum application payload is smaller than 127 bytes after MAC/security overhead

## Slide 50
Part D — IEEE 802.15.4
50/60
Energy Detection and CCA
Before MAC protocols, the PHY can sense energy or channel occupancy.
Energy Detection
Measures received energy in the selected channel. It does not identify the transmitter, protocol, or decodability.
Clear-Channel Assessment
Determines whether the channel appears busy before transmission. It supports CSMA/CA but cannot prevent every collision.
CCA sees the channel at the sender, not necessarily at the receiver

## Slide 51
Part D — IEEE 802.15.4
51/60
2.4 GHz coexistence
IEEE 802.15.4 shares spectrum with louder neighbors.
Wi‑Fi / IEEE 802.11
Bluetooth
Other IEEE 802.15.4 networks
Microwave ovens
Industrial equipment
Proprietary wireless devices
Consequences
Increased packet loss, reduced PRR, retransmissions, higher energy, longer delay, route changes and apparent asymmetry.

## Slide 52
SECTION
Part E: Cooja lab with Contiki 3.0
Old Instant Cooja inside VMware — no Contiki-NG assumptions.
Week 2 section break
52/60

## Slide 53
Part E — Cooja/Contiki 3.0
53/60
Toolchain reality for this course
Everything runs in Instant Contiki 3.0 inside VMware.
Use
Instant Contiki 3.0 VM
VMware Player/Workstation
Old Cooja simulator
Contiki 3 examples
Avoid
Contiki-NG APIs
New TSCH tutorials
Modern Docker-only instructions
Changed directory names
Start Cooja
cd ~/contiki/tools/cooja
ant run
Alternative from project:
make file.cooja TARGET=cooja
In labs, tool reproducibility beats latest-version elegance

## Slide 54
Part E — Cooja/Contiki 3.0
54/60
Old Cooja radio media
Simulation result = code + topology + radio model.
UDGM: Distance Loss
Simple range/interference behavior; good for first experiments and visualizing distance effects.
Directed Graph Radio Medium
Manually define directional links; ideal for asymmetry demonstrations.
MRM / richer models
If present in your VM, use carefully; still an approximation, not field truth.

## Slide 55
Part E — lab setup
55/60
Lab objective
Measure RSSI, LQI and PRR in old Cooja and explain why they disagree.
Build one sender and one receiver application
Send numbered packets periodically
Log sequence number, RSSI, LQI and sender ID
Move nodes and modify radio-medium settings
Calculate PRR over a defined observation window
Explain metric disagreement using propagation concepts
Deliverable
One-page lab report with screenshot, topology, radio model, table of results and interpretation.

## Slide 56
Part E — lab setup
56/60
Suggested lab folder and files
Keep it simple and compatible with old Contiki.
~/contiki/examples/week2-radio/
Files
week2-sender.c
week2-receiver.c
Makefile
week2-template.csc
results-template.csv
Makefile idea
CONTIKI = ../..
all: week2-sender week2-receiver
include $(CONTIKI)/Makefile.include

## Slide 57
Part E — lab code
57/60
Receiver-side logging idea
Old Contiki/Rime style: log packet attributes.
static void recv(struct broadcast_conn *c,
const linkaddr_t *from) {
uint16_t seq = packetbuf_attr(PACKETBUF_ATTR_PACKET_ID);
int rssi = packetbuf_attr(PACKETBUF_ATTR_RSSI);
int lqi = packetbuf_attr(PACKETBUF_ATTR_LINK_QUALITY);
printf("from=%u.%u seq=%u rssi=%d lqi=%d\n",
from->u8[0], from->u8[1], seq, rssi, lqi);
}
Exact attribute behavior can differ by radio model; students must report their Cooja radio medium.

## Slide 58
Part E — lab experiment
58/60
Lab Part A — baseline direct link
Start with a clean two-node topology.
1
2
Sender → Receiver
Radio medium: UDGM Distance Loss
Place nodes close enough for high PRR
Run for at least 100 packets
Export or copy receiver logs
Calculate PRR from sequence numbers
Baseline first; chaos later

## Slide 59
Part E — lab experiment
59/60
Lab Part B — distance and transitional region
Move the receiver gradually and watch metrics change.
PRR vs. distance
Student task
For each position, record average RSSI, average LQI, received count, missing count and PRR. Identify connected, transitional and disconnected regions.
Do not infer real-world range directly from Cooja distance

## Slide 60
Part E — useful links
60/60
Useful links and lab references
Stable references for the old Contiki/Cooja workflow and radio background.
Contiki 3.0 release
https://github.com/contiki-os/contiki/releases/tag/3.0
Cooja introduction wiki
https://github.com/contiki-os/contiki/wiki/An-Introduction-to-Cooja
CC2420 datasheet
https://www.ti.com/lit/ds/symlink/cc2420.pdf
IEEE 802.15.4 topic
https://standards.ieee.org/ieee/802.15.4/
Course lab rule
Run labs only in Instant Contiki 3.0 / old Cooja / VMware unless explicitly told otherwise.
Week 3 bridge
Energy analysis starts with radio states: transmit, receive/listen, idle and sleep.
Week 2 mantra: measure the link, do not assume the link