## Slide 1
Week 2 Cooja Lab
Radio Propagation & Link Quality
Contiki 3.0 · Old Cooja · Sky motes · Rime broadcast
hands-on simulator work
not a written problem set
Notes: Open by framing the class as a 70-minute guided experiment. Students will manipulate the radio environment directly, not solve a theory sheet.

## Slide 2
LECTURE CONTEXT
Why this lab exists
WSN Week 2 · Contiki 3.0 / Cooja
2
Core lesson A wireless link is not just “connected” or “disconnected”. It is a time-varying communication process with a probability of successful packet delivery.
• Distance affects average received power, but does not fully determine link reliability.
• RSSI, LQI, and PRR measure different things.
• The selected Cooja radio medium changes what students observe.
• One sender + one receiver is enough to make the PHY/link-layer behavior visible.
move a node
watch packets
count losses
compare models
Notes: Connect this to Week 2: path loss, RSSI, LQI, PRR, transitional region. The lab is intentionally small so the radio effects are not hidden by routing complexity.

## Slide 3
WHAT STUDENTS SHOULD DO
Learning outcomes
WSN Week 2 · Contiki 3.0 / Cooja
3
By the end
Evidence in lab
Start and configure old Cooja
ant run, new simulation, Sky motes
Send numbered packets
TX seq=... printed by sender
Observe received packets
RX seq=... RSSI=... LQI=...
Create packet loss
missing sequence numbers
Estimate PRR
received / sent
Compare propagation models
UDGM vs MRM behavior
Notes: Keep grading light: completion, screenshots, and a small measurement table. The objective is hands-on familiarity.

## Slide 4
SYSTEM OVERVIEW
Lab architecture
WSN Week 2 · Contiki 3.0 / Cooja
4
Sender
Sky mote 1
Receiver
Sky mote 2
Traffic pattern Sender broadcasts one sequence number per second. Receiver prints the sequence number plus RSSI and LQI for each successfully received packet.
Why broadcast? It avoids routing, addressing, and IPv6 configuration. The lab remains focused on radio propagation and link quality.
Notes: Point out that this is intentionally not RPL, not 6LoWPAN, and not application-layer networking. Broadcast keeps the experiment clean.

## Slide 5
CONTIKI 3.0
Version-specific setup
WSN Week 2 · Contiki 3.0 / Cooja
5
• Use classic Contiki 3.0, not Contiki-NG.
• Launch Cooja with Apache Ant: ant run.
• Use Sky motes through MSPSim.
• Use Rime broadcast, not NullNet.
• Use UDGM Distance Loss and optional MRM.
cd ~/contiki-3.0/tools/cooja
ant run
Instructor warning Fix MSPSim before class. Do not let the lab become a dependency-repair session.
Notes: Emphasize the version change: this deck is for old Contiki 3.0/Instant Contiki. The command and code differ from Contiki-NG.

## Slide 6
BEFORE CLASS
Instructor pre-lab checklist
WSN Week 2 · Contiki 3.0 / Cooja
6
cd ~/contiki-3.0
git status
# If it is a git repository:
git submodule update --init --recursive
# Then start Cooja:
cd tools/cooja
ant run
MSPSim error symptom “Could not find the MSPSim build file. Did you run git submodule update --init?” means Sky motes cannot be emulated yet.
Student handout choice Keep this repair procedure out of the student version unless needed. Fix the VM/image once.
Notes: This slide is instructor-facing. Decide whether to hide it when exporting a student-facing handout.

## Slide 7
LAB MATERIALS
Folder and files
WSN Week 2 · Contiki 3.0 / Cooja
7
~/contiki-3.0/examples/week2-radio/
├── sender.c
├── receiver.c
└── Makefile
• Students browse to sender.c and receiver.c from Cooja.
• Compile each as a separate Sky mote type.
• Create exactly one sender and one receiver.
• Save simulations as .csc files when instructed.
Practical choice Provide the files. Do not ask students to type C code during the 70-minute lab.
Notes: The C code is included in later slides and should also be distributed as files.

## Slide 8
STUDENT STEPS
Create the Cooja simulation
WSN Week 2 · Contiki 3.0 / Cooja
9
File
New simulation
Name: Week2-Radio
UDGM Distance Loss
• Launch from ~/contiki-3.0/tools/cooja.
• Choose “Unit Disk Graph Medium (UDGM): Distance Loss”.
• Keep the simulation simple: two Sky motes only.
• Open Mote Output and Network/Visualizer immediately.
cd ~/contiki-3.0/tools/cooja
ant run
Notes: UDGM is intentionally used first because its simplifications are visible and teachable.

## Slide 9
STUDENT STEPS
Create the two Sky mote types
WSN Week 2 · Contiki 3.0 / Cooja
10
Mote type
Source file
Quantity
Sender
/home/user/contiki-3.0/examples/week2-radio/sender.c
1
Receiver
/home/user/contiki-3.0/examples/week2-radio/receiver.c
1
• Motes → Add motes → Create new mote type → Sky Mote.
• Compile sender.c, then create one sender.
• Compile receiver.c, then create one receiver.
• Place sender left, receiver right.
Sender
Sky mote 1
Receiver
Sky mote 2
Notes: If Sky Mote is missing, the MSPSim submodule is still broken.

## Slide 10
CODE PARAMETER
Parameter: Rime broadcast channel
WSN Week 2 · Contiki 3.0 / Cooja
11
broadcast_open(&broadcast, 129, &broadcast_call);
What 129 means It is the Rime broadcast channel identifier used by both sender and receiver. Both sides must use the same value to hear each other.
Teaching point This is not a physical IEEE 802.15.4 channel number. It is a software-level Rime channel ID.
• Change it only if both programs use the same new value.
• Mismatch = no receiver output even if motes are close.
Notes: Students often confuse Rime channel IDs with PHY channels. Make the distinction clear.

## Slide 11
CODE PARAMETER
Parameter: packet interval
WSN Week 2 · Contiki 3.0 / Cooja
12
etimer_set(&timer, CLOCK_SECOND);
...
etimer_reset(&timer);
One packet per second A slow interval makes sequence numbers readable in Mote Output. It also avoids turning the lab into a congestion experiment.
• Good for manual observation: students can count packets.
• Shorter intervals create more traffic and can blur the PHY/link lesson.
• For this lab: keep it at CLOCK_SECOND.
Notes: The interval is a pedagogical parameter as much as a technical one. Keep it slow for the first lab.

## Slide 12
CODE PARAMETER
Parameter: sequence number
WSN Week 2 · Contiki 3.0 / Cooja
13
static uint16_t seq = 0;
...
seq++;
packetbuf_copyfrom(&seq, sizeof(seq));
printf("TX seq=%u\n", seq);
Why it matters Sequence numbers allow students to detect loss without packet sniffers. If RX jumps from 8 to 10, packet 9 was missed.
RX seq=7
RX seq=8
RX seq=10 ← seq=9 missing
Notes: Tie this directly to PRR: PRR is not guessed; it is counted from observed sequence numbers.

## Slide 13
LINK-QUALITY METRIC
Parameter: RSSI
WSN Week 2 · Contiki 3.0 / Cooja
14
rssi_raw = (int8_t)packetbuf_attr(PACKETBUF_ATTR_RSSI);
rssi_dbm = ((int16_t)rssi_raw) - 45;
Interpretation RSSI is received signal strength. Less negative usually means stronger: −60 dBm is stronger than −90 dBm.
Example RSSI
Informal reading
−50 dBm
very strong
−70 dBm
moderate
−85 dBm
weak
−95 dBm
very weak
Notes: Do not oversell the exact numbers. They are illustrative and radio/platform dependent.

## Slide 14
LINK-QUALITY METRIC
Parameter: LQI
WSN Week 2 · Contiki 3.0 / Cooja
15
lqi = packetbuf_attr(PACKETBUF_ATTR_LINK_QUALITY);
printf("RX seq=%u RSSI=%d dBm LQI=%u\n",
seq, rssi_dbm, lqi);
Interpretation LQI is quality information for a packet that was actually received. It is implementation-specific, so do not compare it as a universal physical unit.
• Useful for observing individual received packets.
• Unavailable for packets that were never decoded.
• A high LQI on one packet does not prove high long-term PRR.
Notes: Stress the difference: LQI describes a received frame; PRR describes many transmissions.

## Slide 15
LINK-QUALITY METRIC
Parameter: PRR measurement window
WSN Week 2 · Contiki 3.0 / Cooja
16
PRR = received packets / transmitted packets
In this lab Use 10-packet windows for quick movement tests and one 20-packet window for the reduced-success experiment.
Window
Use
10 packets
quick observation while moving
20 packets
small PRR measurement
30+ packets
better but slower estimate
Teaching point PRR is empirical. It requires multiple transmissions and depends on the chosen observation window.
Notes: Use small windows for time management. Explain that larger windows are more stable but slower.

## Slide 16
RADIO MEDIUM
UDGM parameters: what students change
WSN Week 2 · Contiki 3.0 / Cooja
17
Parameter
Role in lab
Transmission range
inside this radius, packets may be received
Interference range
larger area where transmissions may disturb reception
TX success ratio
probability a transmission succeeds at sender side
RX success ratio
probability a receivable packet is delivered at receiver side
Default classroom setting Start with a clean, almost deterministic link: TX success = 1.0, RX success = 1.0, transmission range ≈ 20 m.
Loss experiment setting Then reduce RX success to about 0.6 while keeping the motes stationary. This creates visible missing sequence numbers.
Notes: Explain that these are simulation controls, not exact physical constants. The point is to see what each knob does.

## Slide 17
RADIO MEDIUM
UDGM: what it teaches and hides
WSN Week 2 · Contiki 3.0 / Cooja
18
Sender
Sky mote 1
Receiver
Sky mote 2
Teaches well The idea of radio range and the effect of crossing a communication boundary.
Hides badly Real links do not usually have a perfectly sharp boundary. Transitional links can lose and receive packets at the same position.
How we use it First as a simple visual baseline; then we deliberately show its limitation.
Notes: Do not present UDGM as realism. Present it as the simplest controlled model.

## Slide 18
STUDENT ACTIONS
Hands-on A: first packets
WSN Week 2 · Contiki 3.0 / Cooja
19
• Press Start.
• Watch TX seq=... from sender.
• Watch RX seq=... RSSI=... LQI=... from receiver.
• Pause after about 10 packets.
• Verify that receiver sequence numbers follow sender sequence numbers.
1: TX seq=1
1: TX seq=2
1: TX seq=3
2: RX seq=1 RSSI=-63 dBm LQI=104
2: RX seq=2 RSSI=-64 dBm LQI=103
2: RX seq=3 RSSI=-64 dBm LQI=105
Notes: This is their first success checkpoint. Make sure every student can see both sender and receiver output.

## Slide 19
STUDENT ACTIONS
Hands-on B: distance positions
WSN Week 2 · Contiki 3.0 / Cooja
20
Position
Action
Run length
Close
Place receiver close to sender
10 packets
Medium
Drag receiver farther away
10 packets
Near edge
Move receiver near range boundary
10 packets
Student instruction Do not calculate averages. Record one typical RSSI/LQI range from what you actually see.
Instructor emphasis They must physically drag the receiver. This is the point of the lab.
Notes: Keep the workflow tactile: move node, start, watch, pause, record.

## Slide 20
WORKSHEET
Student recording table
WSN Week 2 · Contiki 3.0 / Cooja
21
Position
Sent
Received
Typical RSSI
Typical LQI
Close
10
Medium
10
Near edge
10
Reduced-success link
20
Minimal writing The table exists only to force observation. Do not turn this lab into a written exam.
Notes: The final student submission can be this table plus screenshots.

## Slide 21
STUDENT ACTIONS
Hands-on C: cross the boundary
WSN Week 2 · Contiki 3.0 / Cooja
22
inside range
packets arrive
drag outside
RX stops
drag inside
• Start with receiver just inside the transmission range.
• Watch approximately five packets arrive.
• Drag the receiver outside while the simulation is still running.
• Sender continues printing TX; receiver output stops.
• Drag back inside and observe reception resume.
Notes: This is the slide students remember. The boundary makes UDGM’s simplification very obvious.

## Slide 22
STUDENT ACTIONS
Hands-on D: create controlled packet loss
WSN Week 2 · Contiki 3.0 / Cooja
23
Step
Parameter
Value
1
TX success
1.0
1
RX success
1.0
2
TX success
1.0
2
RX success
0.6
TX seq=34
TX seq=35
TX seq=36
TX seq=37
TX seq=38
RX seq=34
RX seq=36
RX seq=38
Important Do not move the motes during this step. The only change should be the radio-medium success ratio.
Notes: This distinguishes physical movement from probabilistic reception. Same geometry, different delivery.

## Slide 23
STUDENT ACTIONS
Hands-on E: PRR from observed packets
WSN Week 2 · Contiki 3.0 / Cooja
24
PRR = received / sent
Example: 14 packets received out of 20
PRR = 14 / 20 = 0.70
Their task Use the reduced-success experiment. Count received packets from the Mote Output and compute one PRR value.
Experiment
Sent
Received
PRR
Reduced-success link
20
Notes: This should be quick. They are not analyzing statistics; they are turning observations into a basic metric.

## Slide 24
RADIO MEDIUM
MRM: optional comparison model
WSN Week 2 · Contiki 3.0 / Cooja
25
• Create a second simulation named Week2-MRM.
• Choose Multi-path Ray-tracer Medium if available.
• Add the same Sender and Receiver Sky mote types.
• Open MRM Area Viewer / Formula Viewer if present.
• Move the receiver and observe changes in output and visualization.
Instructor framing MRM is not a perfect physical world either. It is a richer propagation abstraction than UDGM and helps students see that radio-medium choice matters.
Time rule If class is slow, skip MRM. The core lab is still complete with UDGM + controlled loss.
Notes: Use MRM as comparison, not as a rabbit hole. Do not ask students to tune ray-tracing equations in this lab.

## Slide 25
INSTRUCTOR TALK TRACK
Parameter lecture: transmission range
WSN Week 2 · Contiki 3.0 / Cooja
26
Meaning in UDGM A configured radius around a transmitting mote. Inside it, packets may be delivered; outside it, they are not delivered by the model.
Dangerous interpretation Do not say this is the real-world range of a TelosB/Sky mote. It is a simulation parameter.
Sender
Sky mote 1
Receiver
Sky mote 2
Notes: Lecture point: simulation knobs are abstractions. The same numeric value may not transfer to a real classroom, corridor, or outdoor deployment.

## Slide 26
INSTRUCTOR TALK TRACK
Parameter lecture: interference range
WSN Week 2 · Contiki 3.0 / Cooja
27
• Transmission range: where a packet can be received.
• Interference range: where a transmission may still disturb another reception.
• This becomes important with more than two motes.
• In today’s two-node lab, keep the focus on transmission range and success ratios.
Simple analogy A person may be too far away to understand clearly, but still loud enough to interrupt someone else nearby.
Do not overuse today Hidden terminals and CCA belong better to the MAC week.
Notes: Mention interference range briefly so the parameter is not mysterious, but do not let it steal the lab.

## Slide 27
INSTRUCTOR TALK TRACK
Parameter lecture: success ratios
WSN Week 2 · Contiki 3.0 / Cooja
28
Ratio
Lab meaning
TX success = 1.0
sender side does not inject random loss
RX success = 1.0
receiver side delivers all in-range packets
RX success = 0.6
roughly 60% of otherwise receivable packets pass
Why use this knob? It lets students observe PRR and missing sequence numbers even without a complicated multipath/fading setup.
Careful wording Do not promise exactly 12 of 20 packets at RX=0.6. It is probabilistic.
Notes: This parameter is ideal for a first lab because it creates visible packet loss on demand.

## Slide 28
INSTRUCTOR TALK TRACK
Parameter lecture: RSSI vs LQI vs PRR
WSN Week 2 · Contiki 3.0 / Cooja
29
Metric
Represents
Collected how
RSSI
received power
per received packet
LQI
packet quality estimate
per received packet
PRR
delivery reliability
over many transmissions
One-sentence distinction RSSI tells us how strong the heard packet looked; LQI tells us something about the decoded packet; PRR tells us how often packets arrived at all.
Notes: This slide maps directly to the Week 2 study guide’s comparison table.

## Slide 29
SUBMISSION
Expected student deliverables
WSN Week 2 · Contiki 3.0 / Cooja
30
• Screenshot 1: two Sky motes with UDGM radio range visible.
• Screenshot 2: Mote Output with TX seq and RX seq/RSSI/LQI.
• Screenshot 3: reduced-success or boundary-crossing experiment.
• One completed measurement table.
• One PRR value from the reduced-success experiment.
Experiment
Sent
Received
Observation
Close UDGM
10
Medium UDGM
10
Near-edge UDGM
10
Reduced success
20
Notes: This keeps assessment aligned with hands-on work.

## Slide 30
COMMON ERRORS
Troubleshooting: Cooja does not start
WSN Week 2 · Contiki 3.0 / Cooja
31
BUILD FAILED
Could not find the MSPSim build file.
Did you run "git submodule update --init"?
cd ~/contiki-3.0
git submodule update --init --recursive
cd tools/cooja
ant run
Meaning MSPSim is missing, so Cooja cannot emulate Sky motes.
Best practice Repair the VM before lab day. Keep students focused on radio experiments.
Notes: If this happens during class, pause and fix centrally if possible.

## Slide 31
COMMON ERRORS
Troubleshooting: no receiver output
WSN Week 2 · Contiki 3.0 / Cooja
32
Symptom
Check
Only TX seq appears
receiver compiled from receiver.c?
RX never appears
same Rime channel 129 on both sides?
RX stops at edge
receiver outside transmission range?
Compilation fails
file path and CONTIKI variable in Makefile
Sky mote unavailable
MSPSim/submodule problem
Instructor shortcut Keep a working .csc simulation ready as backup.
Notes: A prepared .csc saves the class if several students get stuck.

## Slide 32
APPENDIX
Code map
WSN Week 2 · Contiki 3.0 / Cooja
33
sender.c
broadcast_send
radio medium
receiver.c
packetbuf_attr
• sender.c periodically creates a sequence number and broadcasts it.
• Cooja radio medium decides whether the frame reaches the receiver.
• receiver.c prints the received sequence number, RSSI, and LQI.
• Makefile builds both programs under Contiki 3.0.
Notes: Transition to code appendix. These slides can be used when explaining what the provided files do.

## Slide 33
CODE APPENDIX
sender.c — includes and setup
WSN Week 2 · Contiki 3.0 / Cooja
34
#include "contiki.h"
#include "net/rime/rime.h"
#include "net/packetbuf.h"
#include <stdio.h>
#include <stdint.h>
PROCESS(sender_process, "Radio lab sender");
AUTOSTART_PROCESSES(&sender_process);
static struct broadcast_conn broadcast;
static void
broadcast_recv(struct broadcast_conn *c, const linkaddr_t *from)
{
/* Sender does not process received packets. */
}
static const struct broadcast_callbacks broadcast_call = {
broadcast_recv
};
Notes: Explain PROCESS, AUTOSTART_PROCESSES, the broadcast connection, and the callback structure.

## Slide 34
CODE APPENDIX
sender.c — timer and transmission loop
WSN Week 2 · Contiki 3.0 / Cooja
35
PROCESS_THREAD(sender_process, ev, data)
{
static struct etimer timer;
static uint16_t seq = 0;
PROCESS_EXITHANDLER(broadcast_close(&broadcast);)
PROCESS_BEGIN();
broadcast_open(&broadcast, 129, &broadcast_call);
etimer_set(&timer, CLOCK_SECOND);
while(1) {
PROCESS_WAIT_EVENT_UNTIL(etimer_expired(&timer));
seq++;
packetbuf_copyfrom(&seq, sizeof(seq));
broadcast_send(&broadcast);
printf("TX seq=%u\n", seq);
etimer_reset(&timer);
}
PROCESS_END();
}
Notes: Focus on etimer, seq++, packetbuf_copyfrom, broadcast_send, and printf.

## Slide 35
CODE APPENDIX
receiver.c — includes and process setup
WSN Week 2 · Contiki 3.0 / Cooja
36
#include "contiki.h"
#include "net/rime/rime.h"
#include "net/packetbuf.h"
#include <stdio.h>
#include <stdint.h>
#include <string.h>
PROCESS(receiver_process, "Radio lab receiver");
AUTOSTART_PROCESSES(&receiver_process);
static struct broadcast_conn broadcast;
static void
broadcast_recv(struct broadcast_conn *c, const linkaddr_t *from)
{
uint16_t seq;
int8_t rssi_raw;
Notes: Explain that receiver also opens the same Rime broadcast channel.

## Slide 36
CODE APPENDIX
receiver.c — receive callback and sequence extraction
WSN Week 2 · Contiki 3.0 / Cooja
37
int16_t rssi_dbm;
uint16_t lqi;
if(packetbuf_datalen() >= sizeof(seq)) {
memcpy(&seq, packetbuf_dataptr(), sizeof(seq));
rssi_raw =
(int8_t)packetbuf_attr(PACKETBUF_ATTR_RSSI);
/* CC2420 RSSI uses an approximately -45 dB offset. */
rssi_dbm = ((int16_t)rssi_raw) - 45;
lqi =
packetbuf_attr(PACKETBUF_ATTR_LINK_QUALITY);
printf("RX seq=%u RSSI=%d dBm LQI=%u\n",
seq, rssi_dbm, lqi);
}
}
static const struct broadcast_callbacks broadcast_call = {
Notes: Explain packetbuf_datalen, packetbuf_dataptr, memcpy, and packetbuf_attr.

## Slide 37
CODE APPENDIX
receiver.c — RSSI/LQI print and process loop
WSN Week 2 · Contiki 3.0 / Cooja
38
broadcast_recv
};
PROCESS_THREAD(receiver_process, ev, data)
{
PROCESS_EXITHANDLER(broadcast_close(&broadcast);)
PROCESS_BEGIN();
broadcast_open(&broadcast, 129, &broadcast_call);
while(1) {
PROCESS_YIELD();
}
PROCESS_END();
}
Notes: Explain that PROCESS_YIELD keeps the receiver alive while callbacks handle packets.

## Slide 38
CODE APPENDIX
Makefile
WSN Week 2 · Contiki 3.0 / Cooja
39
CONTIKI_PROJECT = sender receiver
all: $(CONTIKI_PROJECT)
CONTIKI = ../..
include $(CONTIKI)/Makefile.include
• CONTIKI_PROJECT lists the programs to build.
• CONTIKI = ../.. is correct when this folder is under examples/week2-radio.
• Makefile.include supplies the Contiki 3.0 build rules.
Notes: Mention that Cooja compiles from the selected .c file but still uses the build system context.

## Slide 39
APPENDIX
Useful terminal commands
WSN Week 2 · Contiki 3.0 / Cooja
40
# Start Cooja
cd ~/contiki-3.0/tools/cooja
ant run
# Optional: compile from terminal
cd ~/contiki-3.0/examples/week2-radio
make TARGET=sky sender.sky receiver.sky
# Clean build artifacts
make TARGET=sky clean
Classroom practice Students mostly use the Cooja GUI. Terminal compile is useful for instructors and troubleshooting.
Notes: Only show the optional compile command if needed.

## Slide 40
WRAP-UP
Source basis and closing takeaways
WSN Week 2 · Contiki 3.0 / Cooja
41
• The lab follows the Week 2 themes: path loss, RSSI, LQI, PRR, transitional behavior, and Cooja radio models.
• The experiment uses one transmitter and one receiver so students can directly connect motion, radio model, and observed packet delivery.
• The most important observation: RSSI/LQI readings and PRR are related but not interchangeable.
• Simulation parameters are learning tools, not promises about real deployment performance.
End with this line “A wireless link is not a cable. Measure delivery; do not assume it from distance alone.”
Notes: Close by asking students what changed when only the simulator parameter changed and when only the position changed.